## Slide 1: Neutrinos from Stored Muons nSTORM Target Station Conceptual Design 15-April-2013 Kris Anderson Fermilab/Accelerator Division/Mechanical Support Department Target Facilities Group Leader

## Slide 2: • Goal is to utilize prior and existing target station designs and components from successfully operated FNAL target stations (NuMI/NOvA, AP0 Antiproton Source, MiniBoone) • Existing design costs and operational characteristics are well understood • SWF is a significant cost driver for new projects and impact is minimized by utilizing or slightly modifying existing design concepts
nSTORM Target Station Conceptual Design

## Slide 3: • Target station beamline chase with adequate shielding • Active beamline elements include: - Production target - Focusing horn, stripline bus, and power supply - Pair of quadrupole magnets and related power supplies/utilities - Water cooled collimators for quad protection • Support modules for beamline alignment of the above devices • Air handling and radioactive water (RAW) systems • Work cell for hot handling and failed component repair/replacement • Remote handling fixtures and camera system • Hot component storage morgue for device cool-down • Functional civil construction enclosure consistent with providing the means of maintaining Target Station equipment and facilitating adequate operational up-time
Key Elements of vStorm Target Station

## Slide 4: Utilize NuMI /NOvA style horn 1 for focusing pions produced in a NuMI low energy style graphite fin target - NuMI LE style graphite fin target (95cm length x 6.4mm wide) has been successfully operated at beam power of 350kW to 400kW - NuMI horn 1 baseline design for 200kA peak current pulse, 400kW incident beam, and 10M pulse fatigue life (plus an additinal fatigue life safety factor) - Work ongoing to define quadrupole magnet design and requirements
nSTORM Target Station Beamline Elements

## Slide 5: Target for Low Energy Neutrino Spectrum
Graphite Fin Core
6.4 mm wide
Water cooling tube
Backing target out of horn produces neutrinos at higher energies
Fits within the horn.

## Slide 6: Magnetic Horn General Design Features
Large toroidal magnetic field
Requires large current - 200 kAmp
Thin inner conductor, to minimize p+ absorption
Water spray cooling on inner conductor
Depending on Polarity Horn Can
Focus p+ or p-
Outer Conductor
Inner Conductor
Stripline
Drain
Insulating Ring
Spray Nozzle
p+
B
I

## Slide 7
nSTORM Target Station Beamline Elements: NuMI Horn 1
Stripline
Conductors
Spray Nozzles and
Water Supply Lines
Outer
Conductor
Water Scavenge
Tank

## Slide 8: • Utilize NuMI style target chase and positioning modules • Utilize NuMI style hot handling techniques • Target chase shielding steel would be mostly comprise of relatively inexpensive “Duratek” shielding blocks • Target station facility would likely be a variation between NuMI and the AP0 Antiproton Source Target Hall • Need to have an effective plan for handling airborne activation products and tritium control
nSTORM Target Station Conceptual Design Approach

## Slide 9
Target Chase Configuration-
Proposal to Use NuMI Style
Concrete Lined Beamline Chase Walls and Base Provided by Civil
Construction
Beamline Chase Steel Constructed
Using Duratek Steel Blocks

## Slide 10
Target Chase Configuration-
Proposal to Use NuMI Style Components
NuMI Low Energy Target and Associated Beamline Positioning
Module
New NuMI Horn 1 and Beamline Positioning Module Chase Installation

## Slide 11
Target Chase Configuration-
Proposal to Use NuMI Style Components
Downstream end of horn 1 suspended in NuMI target chase by module showing stripline conductors and water scavenge tank surrounded by Duratek steel shield block pile

## Slide 12
Target Chase Configuration-
Proposal to Use NuMI Style Components
NuMI Workcell for Failed Component Replacement
(Image shown is that of new components during installation)

## Slide 13
vStorm Beamline Chase Conceptual Design
Cross-Section: Horn, Module, and Shielding
Duratek
Steel Shielding
Blocks
Poured
Concrete
3ft. Nominal
Thickness
Horn Module
Support Carriage
Cross-Beam
Air Gap Perimeter
For Air Cooling of
Steel Shield Pile

## Slide 14
vStorm Beamline Target Station Plan View
Work is ongoing to provide cost estimates associated with this
proposed facility
Work
Cell
Temporary
Storage
Morgue
Utilities &
Power Supply
Room
Target
Module
Horn
Module
Quads