## Slide 1: LIEBE: Design of a molten metal target based on a Pb-Bi loop at CERN-ISOLDE
T. De Melo Mendonca, M. Delonca, D. Houngbo, C. Maglioni, L. Popescu, P. Schuurmans, T. Stora
(May 21, 2014)

## Slide 2: Outline
Introduction/context
Proposed design
Diffusion simulations
Numerical results
  Heat Exchanger (HEX)
  Beam impact
Conclusion & next steps

## Slide 3: Introduction/context…

## Slide 4: Introduction/context (1)
Some keywords: high power target, short-lived isotopes, …
Collaboration started in May 2012 for the LIEBE (Liquid Eutectic Lead Bismuth Loop Target) project:
WP definition WP holder Coordinator
WP1 : Coordination CERN T. Stora
WP2 : Conceptual Design and simulations SCK-CEN P. Schuurmans
WP3 : Construction, assembly CERN M. Delonca
  WP4 : Instrumentation CERN T. Mendonca
WP5 : Safety and Licensing CEA A. Marchix
WP6 : Target characterization and analysis PSI D. Schumann
WP7 : Radiochemistry SINP S. Lahiri
WP8 : Offline commissioning IPUL K. Kravalis
WP9 : Online operation CERN T. Mendonca
Aim of LIEBE target: validation of conceptual design for the EURISOL direct target by developing a prototype for CERN-ISOLDE.

## Slide 5: Introduction/context (2)
  ISOLDE: on-line isotope mass separator @ CERN
Instantaneous power: ≈ 1 GW
Proton beam from PSB:
1.4 GeV
2 µA
3e13 protons/pulse
Cycle: 1.2 s
3 kW average power

## Slide 6: Introduction/context (3)

## Slide 7: Proposed design…

## Slide 8: Proposed design (1)
Proposed by EURISOL

## Slide 9: Proposed design (2)
Pump/motor
Main loop
Current front end + target
Current target unit
Diameter: 300 mm

## Slide 10: Proposed design - main part (3)
HEX
Filling tank
Pump pipes
Beam
Diffusion chamber
Container *
* D. Houngbo, SCK-CEN
+ heating/isolating elements all along the loop
≈ 650 mm

## Slide 11: Proposed design – HEX (4)
LBE
HEX
“Casserole” in between water and LBE
Water block
LBE circulation

## Slide 12: Proposed design – HEX (5)
5 working temperatures defined in step of 100 ºC
5 inlets on each side
1 outlet on each side
For each working temperature defined, only two inlets are used.
200 ºC
300 ºC
400 ºC
500 ºC
600 ºC

## Slide 13: Diffusion simulations …

## Slide 14: Diffusion simulations (1)
Static units
Diffusion: model from Fujioka et
al. (NIM 186 (1981) 409)
With
Courtesy T. Mendonca, CERN
Diffusion optimized for droplets shape
Need a grid on the container to create the shower
10 mm
Holes diameter: 0.1 mm,
Thickness plate: 0.5 mm
Material: SS304L

## Slide 15: Diffusion simulations (2)
Improvement of diffusion with temperature
177Hg (T1/2= 130 ms) as reference:
  Increasing droplet radius will decrease the released fraction
  Diffusion efficiency of 38% for 100 ms, 44% for 200 ms in the diffusion chamber
Maximum operating temperature limited by vapor pressure of LBE
Diffusion
Courtesy T. Mendonca, CERN

## Slide 16: Diffusion simulations (3)
Conclusions
  Diffusion efficiency is improved with:
    Droplet shape
    Temperature
    Falling time of the droplets (lower outlet velocity, longer falling distance)

## Slide 17: Numerical results…

## Slide 18: Numerical results – HEX (1)
  Need to keep the target at the desired working temperature for temperature ranging from 200 ºC till 600 ºC
+ | -
Beam | Pump
Pump | Radiation
- | HEX
Power contributions:
Pump power extraction
Radiation power extraction
Beam | 330 to 990 W
Pump | 2 200 W

## Slide 19: Numerical results – HEX (2)
Assessment of HEX behavior with CFX
Dimensioning of an HEX:
Problem: The HEX must extract less power @ 600 ºC than @ 200 ºC BUT power extracted depend on the surface of exchange, the average heat exchange coefficient and the temperature of both fluids involved -> need of a variable HEX!
 | Water | LBE
Flow rate (l/s) | 0.22 | 0.23
T inlet (ºC) | 27 | Variable
T outlet (ºC) | < 90 | Variable

## Slide 20: Numerical results – HEX (3)
Example @ 600 ºC
Tmax water = 79 ºC
Tmax LBE = 597 ºC
Summary of results:
 | T max water (ºC) | P extracted (W)
200 ºC | 78 | 3 180
300 ºC | 83 | 3 050
400 ºC | 73 | 2 890
500 ºC | 68 | 2 820
600 ºC | 79 | 2 650

## Slide 21: Numerical results – HEX (4)
Conclusions
  Temperature and power extraction are in the proper range (values have been checked over the full range of temperature, from 200 ºC up to 600 ºC)
  Further analysis must be computed considering bad thermal contact between the different parts
  Prototype will validate the design
  Temperature controlled with heating elements installed all along the loop

## Slide 22: Numerical results – Beam impact (1)
Assessment of beam impact with Fluka &
Ansys Autodyn
Geometry considered
Container: Stainless Steel 304, solid part, Lagrangian part
Liquid: LBE, SPH elements
Use of 40 gauges along beam axis
Isolde beam parameters

## Slide 23: Numerical results – Beam impact (2)
Material definition
Standard variables @ 600 ºC.
  ρ, Cp, k
Shock EOS (Linear model)
Gruneisen model
  Us = shock velocity, = Gruneisen coefficient, = particle velocity, C0 and S = fitting parameters
  Failure mechanism
    Hydrodynamic tensile limit
    2 values considered: -150 kPa and -1.9 GPa (no value available for LBE)
Courtesy E. Noah, Un Geneva

## Slide 24: Numerical results – Beam impact (3)
Analysis for 50 µs (1 pulse = 32.6 µs) – under hydrodynamic tensile limit
Shock waves deposit energy onto the weakest point of the container (grid part).
Stresses up to 350 MPa (Yield = 390 MPa) in less than 1 ms.

## Slide 25: Numerical results – Beam impact (4)
Analysis for 50 µs (1 pulse = 32.6 µs) – over hydrodynamic tensile limit
Cavitation in the liquid will induce splashing of the LBE and projection of droplets with very high velocity in the diffusion chamber.
Deformation scale: *9

## Slide 26: Numerical results – Beam impact (5)
Conclusions & Outlook
  The geometry needs an improvement to avoid resonant shock waves
  Impact of beam onto the container should be further investigated:
    Negligible impact expected
    Need more detailed simulation to prove it
  Simulation must be computed for longer time

## Slide 27: Conclusion & next steps…

## Slide 28: Conclusion & next steps
Preliminary design is available, under optimization
Test of the Heat Exchanger foreseen
Optimization of the irradiation container under beam impact on-going
Off-line tests scheduled in the near future

## Slide 29: Thank you for your attention!

## Slide 30: Thanks to all the contributors…
V. Barozier
A. P. Bernardes
K. Kravalis
F. Loprete
S. Marzari
R. Nikoluskins
F. Pasdeloup
A. Polato
H. Znaidi
… (and many others…)

## Slide 31: Back up slides…

## Slide 32: Introduction/context (4)
Specificity of RIBs (Radioactive Ion Beam) production via the ISOL (Isotope separation on-line) technique: Isolde target unit
Extraction electrode
Extracted ion beam
Primary beam
Target
Transfer line
Ion source
Plasma
Leaks
Release loss
Decay loss
Leaks
Condensation
Decay loss
Leaks
Condensation
Decay loss
Neutrals
Sidebands
Multiply charged
Isotope production
Diffusion
Effusion

## Slide 33: Introduction/context (5)
Specificity of RIBs (Radioactive Ion Beam) production via the ISOL (Isotope separation on-line) technique: Isolde target unit
RIB intensity
[s-1 μA-1]
Cross section
[cm2]
Proton beam intensity
[s-1 μA-1]
Target density
[atom cm-2]
Diffusion+effusion efficiency
Ionization
efficiency
Radioactive ion beam (RIB) intensity:
Target Heating
Diffusion improves with temperature
Transfer line
Heated: decrease adsorption in effusion process
Cooled: trap condensable isobaric contaminants

## Slide 34: Diffusion/effusion simulations (3)
Effusion: Monte Carlo
  The effusion efficiency is dependent on the geometry of the container/diffusion chamber, the sticking time, the mean free path and number of collisions with droplets and surface of containment.
Thanks to T. Mendonca
Sticking times of ~10-12 s – negligible effect in efficiency
Effusion release efficiencies between 22% and 34% for residence times in the diffusion chamber between 100-200 ms
Estimated release efficiencies (diff+eff) of ~ 8% for 100 ms and ~ 15% for 200 ms.

## Slide 35: Concept 5 - Results
Feeder Volume
Irradiation Volume
Static-Pressures (Pa)
Velocity Vectors (m/s)
35
1 kg of LBE in Feeder Volume,
2 feeder grids of 2520 apertures
1-mm or 0.5-mm thick feeder grids
2520 evacuation apertures
1.5-m/s inlet velocity
~0.2-bar pressure drop
Stable uniform flow between 500 K – 1500 K
Houngbo D.- LIEBE project, Computational Fluid Dynamics (CFD) analysis.- Workshop on Radioactive Ion Beam Production and High-Power Target Stations.- Mol, Belgium, 16-18 September 2013.- [Presentation]

## Slide 36: Numerical results – HEX (3)
Example @ 600 ºC
Pressure in water for case LBE @ 200 ºC
Velocity in water and LBE
Tmax water = 79 ºC
Tmax LBE = 597 ºC

## Slide 37: Numerical results – HEX (4)
Summary of results:
Chart: Temperature LBE (Deg C)
| 200 | 300 | 400 | 500 | 600
Case 1 | 3182 | 4902 | 6622 | 8342 | 10062
Case 2 | 1973.9825 | 3041 | 4108.0175 | 5175.0351 | 6242.0526
Case 3 | 1393.5065 | 2146.7532 | 2900 | 3653.2468 | 4406.4935
Case 4 | 1123.3505 | 1730.567 | 2337.7835 | 2945 | 3552.2165
Case 5 | 832.9744 | 1283.2308 | 1733.4872 | 2183.7436 | 2634
 | T max water (ºC) | P extracted (W)
200 ºC | 78 | 3 180
300 ºC | 83 | 3 050
400 ºC | 73 | 2 890
500 ºC | 68 | 2 820
600 ºC | 79 | 2 650
200 ºC
300 ºC
400 ºC
500 ºC
600 ºC