## Slide 1: Rotating Tungsten Helium cooled Target RoTHeTa
Cyril Kharoua
Daniela Ene, Ferenc Mezei, Etam Noah, François Plewinski, Pascal Sabbagh,
Luca Massidda (CRS4, Sardinia)
Peter Sievers (retired from CERN)
Fernando Sordo (ESS-Bilbao)
4th High Power Targetry Workshop
Malmö 2011-05-02
ρθ

## Slide 2: Outline
Some history
Practical motivation for Helium cooling
Practical motivation for Granular Target
Practical motivation for Rotating Target
Main parameters of the RoTHeTa
Neutronic performance
Thermo-Mechanical study
Loop characteristics
Rotating seal
Maintenance
Lifetime
Conclusion

## Slide 3: Some history
Granular Tungsten target helium cooled was first proposed by Peter Sievers for a MW neutrino factory
First we have considered spheres in a stationary target
Optimum configuration for cooling, thermal shock and thermal stress
Heavy cooling requirements (High Pressure!)
Under the ESS condition a rotating wheel, fitted with tungsten rods and cooled with helium is a viable solution…

## Slide 4: Practical Motivation for Helium Cooling
Objectives:
  Avoid Liquid metal technology
  Avoid Water cooling / corrosion issue related to tungsten target and therefore avoid cladding
Advantages:
  Known technology
  Low activity in the cooling fluid
  Leak tightness
Drawbacks:
  Pressurized gas equipment (3-10bar)
  Leak tightness

## Slide 5: Practical Motivation for Granular Target
Objectives:
  Allows cooling fluid to remove heat within the target (directly where it is deposited)
Advantages:
High density target (75% to 90% of pure tungsten)
  No thermal shock and low stress level
  Flexible target material (choice, arrangement, geometry…)

## Slide 6: Practical Motivation for a Rotating Target
Objectives:
  Increase lifetime (window, tungsten…)
  Alleviate the heat removal
Advantages:
  Dilution of specific activity and after heat
  Less frequent maintenance and handling of radioactive material
  Solid waste
  Upgradeable for higher beam power
Drawbacks:
  Not yet proven concept (but we do not need to re-invent the wheel!)
Rotating seals to be adapted from existing solutions
Heavy assembly

## Slide 7: Main Parameters of the Helium Cooled Rotating Granular Target
A 2.5GeV elliptic Gaussian beam with an RMS of x= 5 cm and y= 1.5 cm (beam footprint at 4 of 20cm x 6cm), an average power of 5 MW, pulsed at 20 Hz
The wheel is rotating at 30RPM (0.5Hz)
The energy deposition calculated with FLUKA gave a maximum Power density (time average for 1/40 of the wheel) of 75W/cm3 (40 times less than in the static target case).
External wheel diameter is150 cm and internal diameter of 50 cm. The helium is blown over the total surface continuously.
Initially rods of 2cm diameter, now 1cm diameter

## Slide 8: Neutronic performance
Brightness at 5 MeV (left) and at 10 MeV (right) on the moderator surface for a 1ms pulse length.
The rotating target made of rod cooled by helium will allow a density of 90% of the raw material, which shall give a performance close to the pure tungsten configuration.
courtesy F. Sordo et al.

## Slide 9: Neutronic performance
Franz Gallmeier investigation (previous TSCS meeting) extended
  Rotating target configuration (run though optimization loop)
  Extrapolation with density (not so accurate)
Tungsten is the most favourable target material, and its dilution is not affecting significantly the neutron production
Element | Effective density | Φcold@10m | Φcold@10m | Φcold@10m | Comment
 | (1/cm3) | (n/cm2/prot.) | Perf in % vs. Best | Loss in % vs. Best | 
W | 19.4 | 6.28E-08 | 100.00% | 0.00% | Calculated
Sphere pure W | 14 | 5.66E-08 | 90.07% | 9.93% | Calculated
Sphere Densimet (*) | 13.875 | 5.61E-08 | 89.26% | 10.74% | Educated guess
Rods Densimet (*) | 16.65 | 6.06E-08 | 96.47% | 3.53% | Educated guess
*DENSIMET is a tungsten alloy with appropriate properties
courtesy F. Gallmeier

## Slide 10: Thermo-mechanical study 2cm Rods
            With a He-cooling circuit set at: Po = 10 Bar, v(He) 8 m.s-1(mass flow of about 20kg/s!!! Which could reduced by tuning it for different zones)
                The peak temperature in the hottest rods is about 577°C (Inlet Temperature was 200°C)
                Helium ∆Tbulk=30K
                Stress in the rods is low even in a fatigue regime (endurance), about 30 to 50 MPa
Chart: 

## Slide 11: Thermo-mechanical study
            He in inlet is at 200°C and exit at about 230°C
            Pressure drop is about 0.2bar and Pumping power about 250kW
Helium Inlet
Helium Outlet
Rotation axis

## Slide 12: Thermo-mechanical study 1cm Rods
            With a more moderate He-cooling circuit (Po = 3 Bar, inlet v(He) of 4 m.s-1, mass flow of 3kg/s)
                The peak temperature in the hottest rods is about 485°C
                Helium ∆Tbulk= 200K
                Stress in the rods is very low even in a fatigue regime (endurance), about 10 to 20 Mpa
Chart: Maximum temperature vs. Time

## Slide 13: Thermo-mechanical study 1cm Rods
For 3kg/s mass flow rate for 3 bar He
Here the pressure drop is 0.1bar equivalent to 62kW of pumping power.

## Slide 14: Cross flow configuration
H2
No contact labyrinth
(Pump outside)
He:  0.3 m3,  10 bar
He:  5 m3, > 1 bar
H2O
W
Containment with flange connection of target trolley & utilities
p

## Slide 15: Thermo-mechanical study Cross flow configuration
Chart: Volume Fraction of Tungsten vs. Space between rods for 2cm diameter rods
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.2000000000000002 | 2.2999999999999998 | 2.4
 | 0.9069 | 0.82258 | 0.7495 | 0.68575 | 0.62979 | 0.58042 | 0.53663 | 0.49761 | 0.4627 | 0.43134 | 0.40307 | 0.37748 | 0.35426 | 0.33311 | 0.31381 | 0.29613 | 0.27991 | 0.26498 | 0.25122 | 0.2385 | 0.22672 | 0.2158 | 0.20565 | 0.19619 | 0.18738
 | 17.4578 | 15.8348 | 14.4279 | 13.2006 | 12.1235 | 11.173 | 10.3301 | 9.5791 | 8.9071 | 8.3034 | 7.759 | 7.2665 | 6.8195 | 6.4124 | 6.0408 | 5.7005 | 5.3882 | 5.1009 | 4.836 | 4.5911 | 4.3645 | 4.1542 | 3.9587 | 3.7767 | 3.607
Transverse cross flow is under estimation
The objective is to use a lower mass flow rates and increase the bulk ∆T in Helium
First estimation show the possibility to consider 2cm rods with 1mm gap (82%of the full W density).
  Mass flow rates is about 3kg/s
  ∆Tbulk=200K
  Tmax in He=310°C
  ∆P≈1bar (VDI WärmeAtlas)

## Slide 16: Helium loop Pressure drop estimation
The main component of the loop to be considered for the overall pressure head required at the pump are:
            The target material (see previous slides)
            The target shaft and other straight pipe (Half of the target)
            The Inlet rotating seals and outlet rotating seals
            The filters (Half of the target)
            The heat exchanger (Half of the target)
The Inlet and Outlet rotating seals could be assumed to have the same pressure drop
The Heat exchanger could be assumed to have half of the pressure drop seen in the target material

## Slide 17: Helium loop Pressure drop estimation
 | Pressure drop [bar] | 
The target material | 0.1 | 
The target shaft and other straight pipe | 0.05 | 
The Inlet rotating seals | 0.1 | 
The outlet rotating seals | 0.1 | 
The filters | 0.05 | 
The heat exchanger | 0.05 | 
 | 0.45 | Total
Pumping Power | 282.7 kW | 
Preliminary estimation
A preliminary assessment could give indication of the pressure drop in the main component of the loop, for Helium flowing at 3kg/s and 3bar for a global volume of 2m3

## Slide 18: Helium Loop and ancillaries loop

## Slide 19: Leak in Rotating Seals
Differential pumping seal with chicanes between 3 bar and atmospheric pressure.
For 0.1mm wide and 50cm long path => at most 2g/s
Pumping of the leak occurs in the last chicane

## Slide 20: Structural analysis
Structural analysis
  Simplified shell model (sector)
  Parameterized model (number of ribs, thickness)
  No thermal loads defined, but gravity, pressure (3bar), rotational velocity
  Simplified post-processing using RCC-MRx criteria

## Slide 21: Structural analysis
The table here summarize the ratio between the acceptable limit (according to RCC-MRx criteria) and the calculated stress.
At 3bar with ribs every 12degree, the minimum thickness of material could be 3mm.
If the pressure can be further reduced, the number of needed ribs (or shell thickness) will be reduced
 |  | Angle between 2 ribs |  |  |  | 
 |  | 9 | 12 | 30 | 45 | 60
Thickness (mm) | 3 | 0.57 | 0.94 | 3.35 | 4.70 | 5.69
 | 4 | 0.32 | 0.53 | 2.24 | 3.57 | 4.51
 | 5 | 0.21 | 0.34 | 1.48 | 2.62 | 3.53
 | 6 | 0.14 | 0.24 | 1.03 | 1.91 | 2.72
 | 7 | 0.11 | 0.17 | 0.76 | 1.42 | 2.08
 | 8 | 0.08 | 0.13 | 0.58 | 1.09 | 1.61

## Slide 22: Maintenance / Layout

## Slide 23: Maintenance / Layout

## Slide 24: Maintenance / Layout
Exchange procedure: a proposal
  Hot cell could be separated from the target station / monolith allowing an operation of it more disconnected from the target operation
  In order to reduce the weight carried by the overhead crane the flask is moved on rails
Basic maintenance is performed on helium circuit (rotating seal, filters, pumps, heat exchanger) by hands on it. The exposure to radiation shall be low.

## Slide 25: Lifetime
The lifetime of such target is supposed to be about 40 times longer than the static target
            As radiation damage will be spread over a large surface/volume
            Fatigue is negligible in the first estimation (non irradiated)

## Slide 26: Conclusion
3bar of pressure seems a viable option with 1cm rods, but further study shall be carried on to confirm and determine the minimum pressure acceptable
Neutron yield is optimum
Some of the main challenges lie in the replacement of the target and its associated downtime
Attention has to be paid to local leak and radioactive release
Special attention has to be paid to the rotating seal

## Slide 27
Thank you for your attention