## Slide 1: Front End – present status
David Neuffer
March 17, 2015

## Slide 2: Outline
Front End for Muon Collider/ Neutrino Factory
  Baseline for MAP
    8 GeV proton beam on Hg target
  325 MHz
    With Chicane/Absorber
Current status
  New targetry
    6.75 GeV on C target
  New Mars generated beams
    Mars ouput much different from previous version
  Buncher rotator with H2 gas
    rematches OK except for loss at beginning of buncher
    can cool and rotatoe simultaneously

## Slide 3: 325MHz System “Collider”
Drift
  20T  2T
Buncher
  Po = 250MeV/c
  PN = 154 MeV/c; N = 10
  Vrf : 0  15 MV/m
    (2/3 occupied)
  fRF : 490  365 MHz
Rotator
  Vrf : 20MV/m
    (2/3 occupied)
  fRF : 364  326 MHz
  N = 12.045
  P0, PN  245 MeV/c
Cooler
  245 MeV/c
  325 MHz
  25 MV/m
  2 1.5 cm LiH absorbers
  /0.75m

## Slide 4: Simulation Results
N :0.15<P<0.35 GeV/c
N: εT<0.03; AL<0.2
N: εT<0.015; AL<0.2
Simulation obtains
  ~0.125 μ/p within acceptances
  with ~60m Cooler
  325 MHz – less power
  shorter than baseline NF
But
  uses higher gradient
  higher frequency rf  smaller cavities
  shorter than baseline NF
  more bunches in bunch train
Useful
cooling

## Slide 5: New Proton Driver parameters
6.75 GeV p, C target
  20  2T short taper
    ~5 m (previously 15)
  X. Ding produced particles at z = 2 m using Mars
  short initial beam
Redo ICOOL data sets to match initial beam
  ref particles redefined
    in for003.dat
    and for001.dat

## Slide 6: Following Scott’s review of front end
Use his initial distributions (obtained by X. Ding)
  8 GeV protons on Hg target
    + and minus
  6.75 GeV protons on C target
  Start beam from z =10 m
    must retranslate into ICOOL reference particles
  Early losses on apertures have already occurred
    23 cm apertures

## Slide 7: ICOOL translation tips
start at “z =10 m”
  (particle time zero is at -1 m)
reference particles
  250 MeV/c ; 154 MeV/c μ+
    165.75 MeV ; 81.1 MeV μ+
  time set by 1 m as 6.75 GeV proton + 10m as μ+
  reference particles set in for003.dat, not for001.dat
01-Feb-2015 X. Ding C 10 m -
0.0 0.250 3.95709E-08 0.0 0.154 4.381345E-08 2
1 1 -3 0 4.354479e-008 1.000000e+000 0.03737 0.03656 0 7.861861e-004 2.558375e-002 2.189235e-001 0 0 0
3 1 -3 0 3.712592e-008 1.000000e+000 -0.03459 -0.11247 0 1.617131e-001 3.506310e-002 4.670452e-001 0 0 0
6 1 -3 0 3.748837e-008 1.000000e+000 0.00304 -0.04460 0 -1.827203e-002 -5.931789e-002 7.809555e-001 0 0 0
10 1 -3 0 3.738523e-008 1.000000e+000 0.07979 0.13944 0 -4.890422e-002 3.733585e-001 1.515145e+000 0 0 0
In ICOOL for001.dat
REFP
2 0 0 0 3
REF2
2 0 0 0

## Slide 8: First simulation results
Simulation results
  Hg target 8 GeV –end of cooling
  ~0.0756 μ+/p; ~0.0880 μ-/p;
  C target 6.75 GeV p
  ~0.0613 μ+/p; ~0.0481 μ-/p;
    0.0726 μ+/p; ~0.0570 μ-/p when multiplied by 8/6.75
  Previous front ends had ~0.1 to ~0.125 μ/p

## Slide 9: Progression of beam through system
z = 11 m
z = 104 m
z = 135 m

## Slide 10: 6.75 GeV p/ C target – 8GeV Hg
Simulations capture typically somewhat less than before
  Big difference in MARS production model
    Mars Inclusive  LAQGSM=1
  Drop in production for ~8 GeV
    Are previous MARS simulations that showed an advantage in production for ~8 GeV still true ?

## Slide 11: Add gas-filled rf in buncher/rotator
34 – 100 atm equivalent
  1.14 MeV/m
    34 atm
  3.45 MeV/m
    100atm
  for 34 atm
    add ~2 MV/m to rf
First tries with ICOOL
  GH in buncher 1 atm
    no change in capture
  Change to 34 atm by
    DENS GH 34.0
  Runs OK but
    reduces capture by 20%
    mostly from low-E muons
      shorter bunch train
no gas
gas
z=135m
gas
z=71m

## Slide 12: Updated gas-filled front end
added gas in rotator
  34 atm
    dE/dx
Increased rf a bit
  Buncher 15z  2+20(z/24) MV/m
  Rotator 20  25
    ref particles decelerate to 230Mev/c
  Cooler 25  28 MV/m
Results are not so bad
  8 GeV Hg +  0.0718 μ/p
  8 GeV Hg -  0.0773 μ/p
  6.75 GeV C +  0.0539 μ+/p
  6.75 GeV C - 0.0430 μ-/p
  ~10% worse than baseline
Tweak of reference particle to fit ICOOL features
  REFP
  2 0.250 0. 1.7 4
  REF2
  2 0.154 0. 7.1
  use phase model 4
    tracks reference particles energy loss in drft/absorber but not in rf
    fixed energy gain.loss in rf
  ref particle acceleration fitted to

## Slide 13: FrontEnd variations
Reduce buncher gas to 17 atm
  ~ 10% better
  back to ~ baseline
  ~0.062 μ+/p
change decelerating rotator back to constant energy rotator
  C  ~0.063 μ+/p
  about the same
  no real advantage/disadvantage in deceleration
Note initial beam is “cooled”, but only in one dimension
  B = 2T – no field flip
  Angular momentum increases
z | εt | ℓ=L/2 | ε+ | ε-
59 | 0.0184 | 0.0054 | 0.0246 | 0.0138
78 | 0,0173 | 0.0059 | 0.0243 | 0.0124
102 | 0.0151 | 0.0074 | 0.0242 | 0.0095

## Slide 14: Effect of new initial distributions
Redo with old initial beams
  2010 Hg 8 GeV p (older MARS)
    0.114 μ+/p
  2014 Hg 8 GeV p (old MARS)
    0.112 μ+/p
  Compare with current BEAM
    Hg 8 GeV p (new MARS)
    0.072 μ+/p
Major difference is newer MARS model

## Slide 15: Beam difference notes
Most of loss in intrinsic performance is from gas in buncher
  Beam enters completely unbunched
  Initial rf is weak; and slowly increases
After some initial loss, SIMILAR TO GAS-FREE BASELINE

## Slide 16: Increase rotator to 100atm
Buncher at 17 atm
  LESS INITIAL LOSS
Increase Buncher gradient to 28 MV/m
  to compensate energy loss
Fairly good performance
  ~0.06 3μ/p (C 6.75)
More cooling in Rotator
  1-D cooling (2T solenoid)
  one mode highly damped
Significant initiation of cooling
  (integrating rotator/cooler)
z | εt | ℓ=L/2 | ε+ | ε-
77 | 0.0176 | 0.0061 | 0.0248 | 0.0124
89 | 0,0144 | 0.0077 | 0.0241 | 0.0087
102 | 0.0128 | 0.0088 | 0.0242 | 0.0066

## Slide 17: Next steps