## Slide 1: Front End – gas-filled cavities
David Neuffer
May 19, 2015

## Slide 2: Outline
Front End for Muon Collider/ Neutrino Factory
  Baseline for MAP
    8 GeV proton beam on Hg target
  325 MHz
    With Chicane/Absorber
Current status
  New targetry
    6.75 GeV on C target
  New Mars generated beams
    Mars ouput much different from previous version
  Buncher rotator with H2 gas
    rematches OK except for loss at beginning of buncher
    can cool and rottoe simultaneously
  beam for Low-energy muons
    150 MeV/c buncher/rotator

## Slide 3: 325MHz “Collider” front end
Drift
  20 T  2 T
Buncher
  Po = 250MeV/c
  PN = 154 MeV/c; N = 10
  Vrf : 0  15 MV/m
    (2/3 occupied)
  fRF : 490  365 MHz
Rotator
  Vrf : 20MV/m
    (2/3 occupied)
  fRF : 364 326 MHz
  N = 12.045
  P0, PN  245 MeV/c
Cooler
  245 MeV/c
  325 MHz
  25 MV/m
  2 1.5 cm LiH absorbers
  /0.75m

## Slide 4: New Proton Driver parameters
6.75 GeV p, C target
  20  2 T short taper
    ~5 m (previously 15)
  X. Ding produced particles at z = 2  10 m using Mars
  short initial beam
Redo ICOOL data sets to match initial beam
  ref particles redefined
    in for003.dat
    and for001.dat

## Slide 5: Following Scott’s review of front end
Use initial distributions (obtained by X. Ding)
  8 GeV protons on Hg target
    + and - particles
  6.75 GeV protons on C target
  Start beam from z = 10 m
    must retranslate into ICOOL reference particles
  Early losses on apertures have already occurred
    23 cm apertures

## Slide 6: ICOOL translation tips
start at “z = 10 m”
  (particle time zero is at -1 m)
reference particles
  250 MeV/c ; 154 MeV/c μ+
    165.75 MeV ; 81.1 MeV μ+
  time set by 1 m as 6,75 GeV proton + 10 m as μ+
  reference particles set in for003.dat, not for001.dat
for003.dat
01-Feb-2015 X. Ding C 10 m -
0.0 0.250 3.95709E-08 0.0 0.154 4.381345E-08 2
1 1 -3 0 4.354479e-008 1.000000e+000 0.03737 0.03656 0 7.861861e-004 2.558375e-002 2.189235e-001 0 0 0
3 1 -3 0 3.712592e-008 1.000000e+000 -0.03459 -0.11247 0 1.617131e-001 3.506310e-002 4.670452e-001 0 0 0
6 1 -3 0 3.748837e-008 1.000000e+000 0.00304 -0.04460 0 -1.827203e-002 -5.931789e-002 7.809555e-001 0 0 0
10 1 -3 0 3.738523e-008 1.000000e+000 0.07979 0.13944 0 -4.890422e-002 3.733585e-001 1.515145e+000 0 0 0
In ICOOL for001.dat
REFP
2 0 0 0 3
REF2
2 0 0 0

## Slide 7: Simulation results
Simulation results
  Hg target 8 GeV –end of cooling
  ~0.0756 μ+/p; ~0.0880 μ-/p;
  C target 6.75 GeV p
  ~0.0613 μ+/p; ~0.0481 μ-/p;
    0.0726 μ+/p; ~0.0570 μ-/p when multiplied by 8/6.75
Previous front ends had ~0.1 to ~0.125 μ/p
  Redo with old initial beams
    2010 Hg 8GeV p
      0.114μ+/p
    2014 Hg 8GeV p
      0.112μ+/p

## Slide 8: Progression of beam through system
z = 11 m
z = 104 m
z = 135 m
o
0.8 GeV
-30m
-50m

## Slide 9: 6.75 GeV p/ C target – 8GeV Hg
Simulations capture typically somewhat less than before
  Big difference in MARS production model
    Mars Inclusive  LAQGSM=1
  Drop in production for ~8 GeV
    Are previous MARS simulations that showed an advantage in production for ~8 GeV still true ?

## Slide 10: Studies on gas-filled rf for buncher/rotator
Stratakis et al. have done cooling channel with gas-filled rf
  ~34 atm H2 to stop breakdown
Extrapolate back to include buncher/rotator
  use gas to suppress breakdown in buncher/rotator
  rf in ~2 T solenoids

## Slide 11: Add gas-filled rf in buncher/rotator
34 – 100 atm equivalent
  1.14 MeV/m
    34 atm
  3.45 MeV/m
    100atm
  for 34 atm
    add ~2 MV/m to rf
First tries with ICOOL
  GH in buncher 1 atm
    no change in capture
  Change to 34 atm by
    DENS GH 34.0
  Runs OK but
    reduces capture by 20%
    mostly from low-E muons
      shorter bunch train
no gas
gas
z = 135 m
gas
z = 71 m
0
-30 m
50 m

## Slide 12: Updated gas-filled front end
added gas in rotator
  34 atm
    dE/dx
Increased rf a bit
  Buncher 15z  2+20(z/24) MV/m
  Rotator 20  25
    ref particles decelerate to 230Mev/c
  Cooler 25  28 MV/m
Results are not so bad
  8GeV Hg +  0.0718 μ/p
  8GeV Hg -  0.0773 μ/p
  6.75 geV C +  0.0539 μ+/p
  6.75 geV C - 0.0430μ-/p
  ~10% worse than baseline
Tweak of reference particle to fit ICOOL features (for 100atm)
  REFP
  2 0.250 0. 1.55 4
  REF2
  2 0.154 0. 6.9
  use phase model 4
    tracks reference particles energy loss in drft/absorber but not in rf
    fixed energy gain.loss in rf
  ref particle acceleration fitted to end at ~245 MeV/c

## Slide 13: FrontEnd variations
Reduce buncher gas to 17 atm
  ~ 10% better
  back to ~ baseline
  ~0.062 μ+/p
decelerating rotator or constant energy rotator?
  C  ~0.063 μ+/p
  about the same
  no real advantage/disadvantage in deceleration
Note initial beam is “cooled”, but only in one dimension
  B = 2 T – no field flip
  Angular momentum increases
z | εt | ℓ=L/2 | ε+ | ε-
59 | 0.0184 | 0.0054 | 0.0246 | 0.0138
78 | 0,0173 | 0.0059 | 0.0243 | 0.0124
102 | 0.0151 | 0.0074 | 0.0242 | 0.0095

## Slide 14: Compare 17/34
600 MeV/c
-20m
40m
34 --- 34 atm
17 --- 34 atm
0.058 μ+/p
0.065 μ+/p
40m
-20m
z = 72 m
z = 108 m
z = 150 m

## Slide 15: Increase rotator to 100atm
Buncher at 17atm
  LESS INITIAL LOSS
With V = 20/25/28
  ~0.059 μ/p (C 6.75)
  ~10% less than 17/34
Increase Rotator gradient to 28 MV/m
  to compensate energy loss
Fairly good performance
  ~0.063 μ/p (C 6.75)
Buncher at 34 atm
  ~0.058 μ/p (C 6.75)
  V = 22/28/30 MV/m
  worse than 17/100 case
More cooling in Rotator
  1-D cooling (2T solenoid)
  one mode highly damped
Significant initiation of cooling
  (integrating rotator/cooler)
  shortens following cooler
z | εt | ℓ=L/2 | ε+ | ε-
77 | 0.0176 | 0.0061 | 0.0248 | 0.0124
89 | 0,0144 | 0.0077 | 0.0241 | 0.0087
102 | 0.0128 | 0.0088 | 0.0242 | 0.0066

## Slide 16: Beam difference notes
Most of loss in intrinsic performance is from gas in buncher
  Beam enters completely unbunched
  Initial rf is weak; and slowly increases
After some initial loss, SIMILAR TO GAS-FREE BASELINE
N: εT<0.03; AL<0.2
0.025
0.05
0.10
0.0
0.125
0.075

## Slide 17: Continue Cooling with H2 Gas
Previous cases used baseline front end cooling
  2 LiH 1.5 cm absorbers per cell
240 atm of H2
  ~8.3 MV/m loss from gas
Preliminary results
  Throughput improved to ~0.068 μ+/6.75 GeV proton C target

## Slide 18: Low-E capture
Capture at low momentum
  prepare beam for low-E μ experiment
Somewhat scaled back version of front end
  30.4m drift
  shorter buncher /rotator
    12 m / 13.5 m
    0  15 MV/m, 15 MV/m
      vacuum rf
  B=2T
Parameters
  150 MeV/c … 100 MeV/c reference particles
  77.8 // 39.8 MeV
Bunch to 150 MeV/c
Cooling at 2 T

## Slide 19: simulation of low-E buncher
Used Ding initial beam
  initial beam cut off at ~70 MeV/c
    21 MeV kinetic energy
  bunch train formed
Cooling from 60m  100m
  longitudinal antidamping
    gL = ~ -0.5
  B=2T , 2cm
  more used to separate captured from uncaptured beam
  ~0.05 μ/p within acceptance ??
    not sure what acceptance criteria to use
0.4
0.4
0.0
0.0
L = 60 m
L = 11 m
0.4 GeV/c
0.0
L = 100 m

## Slide 20: LHC discoveries motivate future research…

## Slide 21: Simulation Results
N :0.15<P<0.35 GeV/c
N: εT<0.03; AL<0.2 c
N: εT<0.015; AL<0.2
Simulation obtains
  ~0.125 μ/p within acceptances
  with ~60m Cooler
  325 MHz – less power
  shorter than baseline NF
But
  uses higher gradient
  higher frequency rf  smaller cavities
  shorter than baseline NF
  more bunches in bunch train
Useful
cooling