## Slide 1
High power target design and operation considerations for kaon production
Philip Pile
Collider-Accelerator Department
Brookhaven National Laboratory
Upton, New York 11973
Snowmass Workshop
on Intensity Frontier
Apr. 17-20, 2013, Brookhaven National Laboratory

## Slide 2: Outline
AGS proton beam, days gone by
LESBIII – a state of the art low energy kaon beam line
Optics considerations for kaon beam line target
LESBIII kaon production target/issues

## Slide 3
PROTON BEAM FY96 FY97 FY98/99 FY2000 FY2001 FY2002
SEB SEB FEB (g-2) SEB FEB (g-2) FEB (g-2) FEB (g-2) SEB
Beam Energy 24 GeV 24 GeV 24 GeV 24 GeV 24 GeV 24 GeV 24 GeV* 22 GeV*
Peak Beam Intensity 62 x 1012 ppp 62 x 1012 ppp 46 x 1012 ppp 72 x 1012 ppp 58 x 1012 ppp 61 x 1012 ppp 63 x 1012 ppp 76 x 1012 ppp
Total protons accelerated 0.9 x 1020 0.4 x 1020 0.1 x 1020 0.9 x 1020 0.4 x 1020 0.5 x 1020 0.6 x 1020 0.7 x 1020
Spill Length/Cycle Time 1.6 sec/3.6 sec 1.6 sec/3.6 sec 2.8 sec/5.1 sec 2.4 sec/5.4 sec
-> Duty Cycle 44% 44% 55% 44%
Spill Structure Modulation
(peak-average) /average 20% 20% 20% 20%
Average Availability
/Best Week 76% / 92% 71% / 79% 58 % / 67 % 71% / 88% 55 % / 83 % 74 % / 87 % 83 % / 88 % 85 % / 97 %
HEAVY ION BEAM Au Au Fe (NASA) Au Fe (NASA) Fe (NASA) Fe (NASA) Fe (NASA)
Beam Energy /nucleon 11 / 4 / 2 GeV 11 / 8 / 6 GeV 1.0 / 0.6 GeV 11 GeV 1.0 / 0.6 GeV 1.0 GeV 1.0 GeV 1.0 GeV
Peak Beam Intensity 4 x 108 Au/p 17 x 108 Au/p 20 x 108 Fe/p 9 x 108 Au/bunch 36 x 108 Fe/p 17 x 108 Fe/p 80 x 108 Fe/p 49 x 108 Fe/p
Spill Length/Cycle Time 1.4 sec/3.6 sec 1.5 sec/4.0 sec 1.2 sec/3.0 sec 0.9 sec/3.3 sec 0.9 sec/3.3 sec 0.9 sec/3.3 sec
-> Duty Cycle 39% 38% 40 % 27% 27% 27%
Spill Structure Modulation
(peak-average) /average <20% <20% <20% <20% <20% <20%
Average Availability 80% 82 % 96 % 81 % 90 % 90 % 97 % 84 %
* Westinghouse
Motor Generator
AGS performance
T. Roser

## Slide 4
Maximum Momentum: 830 MeV/c
Length: 19.6 meters
Angular acceptance: 12 msr
Momentum acceptance: 4% fwhm
Beam Optics: Corrected to third order
Movable Collimators:
  4Jaw Theta-Phi Collimator
  Horizontal Momentum Collimator
  Two Vertical Collimators (Mass Slits)
  Second horizontal collimator at achromatic focus
Electrostatic Separators:
  Two Stage Separation
  < 625kV, 12.7 cm gap x 2.0 meter - #1
  < 560kV, 10.2 cm gap x 2.0 meter - #2
Target: - 2001-2002
  6 cm long platinum silver soldered to
  water cooled copper base
  Maximum ~30 x 1012 per second during spill
Production Angle: 0 degrees
Particle Flux (per 1013, 22 GeV/c protons on target):
  710 MeV/c positive kaons – 2.0 x 106 with 3:1 p/k
LESBIII (E494 beam line)
=adjustable collimators
EXB Wein Filters
in air
in air

## Slide 5
Longitudal acceptance for LESBIII for 800 MeV/c kaons and pions
with EXB separators set to transmit kaons undeflected
TURTLE Simulation
MS1 = 4 mm, MS2 = 5 mm, 4-Jaw and momentum collimators open, vary HS2
Vacuum window
6 cm target

## Slide 6
Longitudal acceptance for LESBIII for 800 MeV/c kaons and pions
with EXB separators set to transmit kaons undeflected
TURTLE Simulation
MS1 = 4 mm, MS2 = 5 mm, 4-Jaw and momentum collimators open, vary HS2
6 cm target
Vacuum window

## Slide 7
MS1 = 4 mm, MS2 = 5 mm, 4-Jaw and momentum collimators open, vary HS2
LESBIII vacuum window
6 cm target

## Slide 8
Turtle simulastion of “cloud pions” in LESBIII, MS1 = 4 mm, MS2 = 5 mm, 4-Jaw and momentum
collimators open, HS2=+/- 1.5 cm, separators set to transmit kaons.
x,y event distribution at center of production target gated by events that make it to the end
Water cooled copper base
Platinum target
Avoid material here that could
become secondary particle source
Note orientation changes (y-y)
with separator field polarities

## Slide 9: Target design considerations
Kaon beam optics
  Short target favored due to longitudal acceptance and kaon beam purity
  E949 settled on conservative 6 cm length
K+ production angle – peaked at 0 deg
Target material
  To maximize kaons flux consistent with short target need dense material, we picked platinum (21.5 g/cm3)
Kaon yield
  Relative yields predicted by G4beamline (relative 600 MeV/c K+’s in forward 45 deg cone with 24 GeV p’s)
    6 cm Pt = 1.0
    6 cm Cu = 0.53
    6 cm C = 0.12
    6 cm Pt 95 GeV protons (ORKA) = 2.4

## Slide 10: Some Target Issues
Inadvertent short spills from the AGS
  In 1997 installed a spill monitor on the AGS extraction beam secondary emission detector (C10 SEC)
  tripped beam off in ~100 msec if rate is > 100 TP/sec..it worked…
Inadvertent high intensity spill
  C-target temperature limit set to trip at 1000 deg C (melting point 1772 deg C).
  Trip point chosen so that stress on the platinum and copper is less than half the maximum hard tensile yield strength as predicted by ANSYS Finite Element calculations.
  Trip response time ~ 200 msec.
  Typical administrative temperature limit for normal spills was 700 deg C.
Target station became contaminated with activated debris from targets
  Target should be enclosed with controlled environment to contain contamination (ours were not)
Unresolved issue:
  Had thermocouple or perhaps deteriorating Pt-Cu bond issue with 2002 target resulting in higher temperature (100 deg C or so) readings for hottest segments late in the run – unresolved as to cause.

## Slide 11
1998-1999 C-target (2490 hours of beam)
24 GeV protons, 2-2.8 sec spill every 4.3-5.1 sec, up to 72 TP available but shared with others,
few x 1019 protons on target, admin. limit set at 50 TP for 2 sec spill at flat top (~700 deg C)
“Workhorse Target”
Pt, 5.1 x 5.1 x 60 mm (w x h x l)
Silver soldered to copper
5 slots, 6 Pt segments

## Slide 12
C-Target: - 2001-2002
  6 cm long 8 segment platinum, 5.1 mm wide x 3.8 mm high
  Platinum silver soldered to water cooled copper base
  Maximum ~30 x 1012 per second @ 22 GeV
beam
Latest (Last) C-Target Design
changes

## Slide 13
18 April 2002
22 GeV protons
56 x 1012 protons per spill
2.2 sec spill every 5.4 sec (41% DF)
Maximum rate on this target was
~70 TP/2.2 sec flat top = 32 TP/sec
Avg Power ~ 45 kW, peak ~110 kW
5R
4L
3R
6L
3R
4L
6L
5R
(as measured with type k thermocouples, drilled and peened into platinum)
2.2 sec

## Slide 14: E949 targets and ORKA
E949 target maximum protons per spill achieved (22 GeV beam)
  ~70 TP/2.2 sec spill with 5.4 sec repetition ~ 700-800 deg C temperature
  Administrative limit was ~30 TP/sec at flat top
  Peak power during spill = 110 kW
  Average power = 45m kW
So with 1000 deg C limit for the 2002 E949 target
  The 2001 target design is good for ~ 90 TP or 40 TP/sec at flat top
ORKA initial plans
  95 GeV protons
  48 TP/ 4.4 sec spill with 10 sec repetition
  Peak power = 166 kW
  Average power = 73 kW
So with E949 2002 target at ORKA
  Temperature ~ 166/110 x (700-800) = 1050-1200 deg C
This target design might be considered as a “day one” target for ORKA….but see next slides…

## Slide 15
Some “Dirty” Laundry…….

## Slide 16
“BEFORE”
“AFTER”
E949, last target design, 2002
~0.5 x 1019 protons
~30-70 x 1012 protons per 2.2 sec spill

## Slide 17
A-Target (E865 - Zeller) after ~10-20TP/spill for a ? years
15 cm long copper target and water cooled base

## Slide 18
Path Forward…

## Slide 19
C-target upgrade – possible approach to a 100 TP Pt target (at ~24 GeV)
Platinum rod segments
Support spiders
Water cooling
Cu base
dimensions in inches
(A. Pendzick)
This target design was under consideration for next generation C-target before DOE HEP lost interest in AGS experiments

## Slide 20
Thanks to I-H Chiang, Steve Kettell Charlie Pearson
and Al Pendzick for helping remember the past!

## Slide 21
Bone yard

## Slide 22
3” thick steel movable shield
6” thick steel fixed shield
LESBIII target front end magnet shield
target

## Slide 23
~ 30-40 TP/spill with interruptions for FEB pulse on demand to the
g-2 experiment, 23 April1997

## Slide 24
1E6, 24 GeV protons on 5mm wide x 3.8 mm high x 60 mm long platinum target
200 mm radius detector 200 mm d/s tgt center
G4beamline

## Slide 25
1E6, 24 GeV protons on 5mm wide x 3.8 mm high x 60 mm long platinum target
200 mm radius detector 200 mm d/s tgt center
G4beamline

## Slide 26
1E6, 24 GeV protons on 5mm wide x 3.8 mm high x 60 mm long platinum target
200 mm radius detector 200 mm d/s tgt center
G4beamline
K+ with 500-700 MeV/c
+/- 10 deg

## Slide 27
1E6, 24 GeV protons on 5mm wide x 3.8 mm high x 60 mm long copper target
200 mm radius detector 200 mm d/s tgt center
G4beamline

## Slide 28
1E6, 24 GeV protons on 5mm wide x 3.8 mm high x 60 mm long carbon target
200 mm radius detector 200 mm d/s tgt center
G4beamline

## Slide 29
1E5, 95 GeV protons on 5mm wide x 3.8 mm high x 60 mm long platinum target
200 mm radius detector 200 mm d/s tgt center
G4beamline

## Slide 30
1E5, 95 GeV protons on 5mm wide x 3.8 mm high x 60 mm long platinum target
200 mm radius detector 200 mm d/s tgt center
G4beamline

## Slide 31
1E5, 95 GeV protons on 5mm wide x 3.8 mm high x 60 mm long platinum target
200 mm radius detector 200 mm d/s tgt center
G4beamline

## Slide 32
1E5, 95 GeV protons on 5mm wide x 3.8 mm high x 60 mm long platinum target
200 mm radius detector 200 mm d/s tgt center
G4beamline