## Slide 1: “Conventional” neutrino beams: Target requirements
Phil Adamson
13th January 2012

## Slide 2: Anatomy of a neutrino beam
Primary proton beam
  Beam window
Target
  Produce π,K
Focusing elements
  Horns sign-select pions
π-
π+
Target
Focusing Horns
2 m
675 m
νμ
νμ
15 m
30 m
120 GeV protons
Decay volume
  π+ -> µ+ νµ
Beam Absorber
  Absorb hadrons
Muons range out in rock
  Neutrinos left

## Slide 3: Introduction
Will discuss the requirements on targets and target halls for high power neutrino beams
  NOvA at 700kW
  LBNE at 700kW
  LBNE+Project X at 2.2MW
  Low energy beam with Project X?
Discussion is mostly generic
  Brand-name advice also available in the room

## Slide 4: An example from NuMI
Solid consistent running delivered 3.2E20 protons to NuMI in FY10
Scheduled summer shutdown
But wait – what’s happening over here

## Slide 5: Annus Horribilis
Got 2.2E20 in FY11, thanks to heroic efforts from target folks (and delay to future projects)
Without target problems would have been 4E20
(NT04)
NT05
NT06
NT01
NT02

## Slide 6: This was NT06
Water cooling lines sprang leak after a few days
Limped on for a month until outer can failed

## Slide 7: Uptime is important!
…but uptime is a Heisenberg number
  When you try to define it, it gets hard to measure
NuMI example: downtime is
  Time removing broken target and installing new target
  Time running at low intensity to try to extend life of dying target

## Slide 8: Design Implications
Neutrino experiments care about integrated neutrino flux over the years)
New target design with 10% flux improvement?
  Great, but if it needs replacing twice a year at 2 weeks or so downtime each, you just lost.
  “Yield per proton vs design conservatism” – Tristan this morning
Probably guaranteed 4 weeks scheduled downtime per year
  Target hall maintenance in shutdown is “free”
  Replace consumable targets etc.
Otherwise, want target hall components to be quick to replace or robust

## Slide 9: Neutrino Flux
Pions from target have few hundred MeV transverse momentum
Place target far away from horn for high energy
  Close (inside) for low
Depth of field etc. makes it a little more complicated
For LBNE, oscillation maxima at 2.5 and 0.8 GeV
  Must place target inside horn (cf. NuMI LE)
Also low energy (cf. BNB)

## Slide 10: Off-axis this isn’t true: NOνA
Off-axis, neutrino energy driven by angle
Adjust focusing to optimize flux
Target goes upstream of horn
0
20

## Slide 11: LBNE Flux optimization
More flux is always good, but in the real world there are tradeoffs
  Zwaska FOM is a useful simple tool, but not intended to be more than that
  What balance of flux required at 0.8 vs 2.5 GeV
  High energy tail causes backgrounds for appearance (NC feeddown)
    LAr detector is better than water
Answer is different for different measurements
Detailed analysis not done
Modifications in target width/length don’t change the design problems much
  Hybrid Light-heavy target is different

## Slide 12: Predicting FD spectra
Oscillation experiments have near detector to measure beam
  But you can’t put a near detector far enough away to make the beam look like a point source rather than a line source
Depend on modelling beam for F/N pred

## Slide 13: Predicting FD spectra
MINOS weights Fluka using ND data at different target positions & horn currents
T2K uses measured meson yields from NA61

## Slide 14: Constraints from FD prediction
Rely on MC to know how spectra at ND and FD should differ
  What’s in MC needs to match what’s in the target hall
    Alignment
    Mass budget
    Beam size
  NuMI requires horn 1, target aligned to 1mm, beam sigma known to better than 0.1mm.
    For LBNE precision disappearance measurement, requirements should be the same (maybe a little tighter?)
    This is less important for appearance
      But need to understand backgrounds (beam )
    beam extrapolate to FD differently (different parent kinematics)
Need to optimize neutrino flux, but also need to know that that is what you have

## Slide 15: Target Alignment
Proton beam scanned horizontally across target and protection baffle
  Also used to locate horns
Hadron Monitor and the Muon Monitors used to find the edges
Measured small (~1.2 mm) offset of target relative to primary beam instrumentation.
Pulse Height in Chamber (arb.)
target
baffle
baffle
target
baffle
baffle
Graphite protection baffle
Graphite target
Water cooling line
21.4 mm
15.0 mm
11.0 mm
6.4 mm
Horizontal Fin
Target
Horn
Baffle
p
p
Notes: Harp on implementation

## Slide 16: Alignment
Need beam-based alignment to be sure of what you’ve got
  NuMI target hall moves when shielding blocks are installed
  Thermal motion
Target, horns need features that can be located with beam scan
  Monitoring alignment whilst running would be great
  Hylen thermometer for NOvA – will it survive 2MW?
Particle yields must be insensitive to natural variation in proton beam position
  Machine dependent
  NuMI has 100um RMS
“Insensitive” is a function of the accuracy of the measurement
  Issue for balls?

## Slide 17: Proton beam alignment
Need to know/measure beam sigma
  Variations greater than 100um are bad
NuMI has Ti SEM wires/foils
  Won’t work for 2MW
Will carbon fibre survive?
Electron beam?

## Slide 18: What’s in your target?
As mentioned, need target & horn model to extrapolate from near to far detector
  Target has to be the same from pulse to pulse
    Different from pbar or muon production target, where you don’t care too much exactly what comes out
    For neutrino beam, the target is part of the physics of the experiment
    Difficult to use liquid or powder target for this

## Slide 19: NuMI 2nd target depletion ( ZXF-5Q amorphous graphite ) NT-02 replaced when spectrum shift became too large.
Decrease as expected when decay pipe changed from vacuum to helium fill
Each point in energy bin
represents ~ 1 month running,
time from 9/2006
Gradual decrease in neutrino rate attributed to target radiation damage
No change when horn 1 was replaced
No change when horn 2 was replaced
Spectrum recovered when
new target was inserted

## Slide 20: What’s in your target?
NuMI observed radiation damage to the graphite of target NT02 (change in neutrino yield)
Effect modelled by removing target fins in MC at maximum dpa from MARS model
NuMI coped with a loss of yield of 10% with a much better than 1% effect on Near -> Far extrapolation
Would prefer to replace a target before it got to that state
Want muon monitor able to track this
  Don’t wait to integrate enough neutrino events to see issue.

## Slide 21: Secondary beam monitoring
Target hall is a hostile environment
  Want multiple complementary beam monitors to distinguish between real effects and dying instrumentation
Hadron monitor downstream of decay pipe
  Survivability at 2MW?
Muon monitors
  Muons and neutrinos come from same decays
    Calibration, drifts, delta rays, …
Temperature rise in absorber is a great independent measure
This kind of monitoring feeds directly into experiment’s systematic error budget

## Slide 22: Project X / LBNE beam
LBNE beam still comes from Main Injector
  New RF system, but not much change
  53 MHz bunches
  Bunch length < 2ns sigma
  1.2s cycle time at 120 GeV
    0.75s at 60 GeV
  1.6E14 protons per spill
    3.3E11 protons per bunch
    Factor 4 increase over now
  2.3 MW
3.5ns

## Slide 23: Summary
Uptime (integrated neutrino yield)
  For a given target, integrated number of protons
  It’s probably worth paying a little pion yield for a more robust target
  Robustness/fast replacement
Repeatability
  Target is the same each pulse
Alignability
  Target hall components can be aligned, and alignment monitored, with beam
Radiation damage
  Model and monitor
Redundant instrumentation
  If you see an effect in hadron monitor and muon monitor, it’s more likely to be real
At 2.2MW, expect the unexpected
  Plan & mitigate risks, but…