## Slide 1
Target System Concept
for a Muon Collider/Neutrino Factory
K.T. McDonald
Princeton University
(May 28, 2014)

## Slide 2
Specifications from the Muon Accelerator Staging Scenario
6.75 GeV (kinetic energy) proton beam with 3 ns (rms) pulse.
1 MW initial beam power, upgradable to 2 MW (perhaps even to 4 MW).
60 Hz initial rep rate for Neutrino Factory;
15 Hz rep rate for later Muon Collider.
The goal is to deliver a maximum number of soft muons,
~ 40 < KE < ~ 180 MeV.

## Slide 3
Target System Concept
Graphite target (ρ ~ 1.8 g/cm3), radiation cooled (with option for convection cooling); liquid metal jet as option for 2-4 MW beam power.
Target inside high-field solenoid magnet (20 T) that collects both µ±.
Target and proton beam tilted with respect to magnetic axis.
Superconducting magnet coils shielded by He-gas-cooled W beads.
Proton beam dump via a graphite rod just downstream of the target.
Some of the proton and /µ transport near the target is in air.

## Slide 4
Stainless-steel target vessel (double-walled with intramural He-gas flow for cooling) with graphite target and beam dump, and downstream Be window.
This vessel would be replaced every few months at 1 MW beam power.
15 T superconducting coil outsert,
Stored energy ~ 3 GJ, ~ 100 tons
5 T copper-coil insert. Water-cooled,
MgO insulated
He-gas cooled W-bead shielding (~ 100 tons)
Proton beam tube
Upstream proton beam window
Target System Concept
Last
Final-Focus
quad

## Slide 5
Target System Optimization

## Slide 6
Target System Optimizations
High-Z favored.
Optima for graphite target: length = 80 cm,
radius ~ 8 mm (with σr = 2 mm (rms) beam radius),
tilt angle = 65 mrad,
nominal geometric rms emittance ε = 5 µm.
β* = σr2 /ε = 0.8 m.
Graphite proton beam dump, 120 cm long, 24 mm radius to intercept most of the (diverging) unscattered proton beam.
The 20 T field on target should drop to the ~ 2 T field in the rest of the Front End over ~ 5 m.

## Slide 7
Issues for Further Study
Thermal “shock” of the short proton pulse
Probably OK for 2 MW and 60 Hz operation;
15-Hz option needs study.
Cooling of target, and the W beads.
Lifetime of target against radiation damage.
Beam windows.
* and beam emittance at the target.
To preserve liquid-metal-jet upgrade option, need related infrastructure installed at t = 0.

## Slide 8
Thermal Issues for Solid Targets
When beam pulse length t is less than target radius r divided by speed of sound vsound, beam-induced pressure waves (thermal shock) are a major issue.
Simple model: if U = beam energy deposition in, say, Joules/g, then the instantaneous temperature rise ∆T is given by ∆T = U /C, where C = heat\ capacity in Joules/g/K.
The temperature rise leads to a strain r/r given by ∆r/r = α ∆T = α U/C,
where α = thermal expansion coefficient.
The strain leads to a stress P (= force/area) given by P = E ∆r/r = E α U/C,
where E = modulus of elasticity.
In many metals, the tensile strength obeys P ≈ 0.002 E, α ≈ 10-5, and C ≈ 0.3 J/g/K,
in which case Umax ≈ P C / E α ≈ 0.002 ∙ 0.3 / 10-5 ≈ 60 J/g.
Graphite @ 1400 C: P = 42.4 Mpa, E = 7.2 Gpa, α = 4.8  10-5, C = 1.4 J/g, Umax ≈ 1700 J/g.
(α ≈ 1  10-5 for carbon-carbon composite)
[A nickel target at FNAL has operated with Umax ≈ 1500 J/g.]
These arguments are from A Short Course on Targetry, KTM,
NuFact03 Summer Institute

## Slide 9
How Much Beam Power Can a Solid Target Stand?
What is the maximum beam power this material can withstand without cracking, for
a 6.75-GeV beam at 15 Hz with area 0.1 cm2?
Ans: MARS15 indicates that the peak energy deposition in a
“pencil” target is essentially just that of dE/dx,
 1.5 MeV/(g/cm2) for graphite.
Now, 1.5 MeV = 2.4 ∙ 10-13 J, so 1500 J/g requires a proton beam
intensity of (1500 J/g)/(2.4 ∙ 10-13 Jcm2/g) ≈ 6 ∙ 1015/cm2.
 Pmax ≈ 15 Hz ∙ 6.75  109 eV ∙ (1.6 ∙ 10-19 J/eV) ∙ (6  1015 /cm2) ∙ 0.1 cm2 ≈ 1 ∙ 107 J/s = 10 MW.
If graphite cracks under singles pulses of > 1500 J/g, then safe up to 10 MW beam power @ 15 Hz.